## Slide 1
Presentation
Jiayu Chen
2024.02.26

## Slide 2
Work Description
Part_1: Template-based IBI Prediction
Part_2: BP-related Features
Part_3: Questions

## Slide 3
Part_1

## Slide 4
      Template-based IBI Prediction
The Background Information of Irregular Heart Rate:
Sinus arrhythmia(窦性心率不齐)
Respiratory sinus arrhythmia: Heart rate increases during inhalation and decreases during exhalation.
Non-respiratory sinus arrhythmia
Judgment Criteria:
Fluctuations in IBI between 10% and 20% are considered relatively normal.
Diagnosis of Heart Rate Abnormality:
When IBI monitoring is entirely accurate and successfully identifies heart rate abnormality.
When IBI monitoring is not entirely accurate but still successfully identifies heart rate abnormality.
Example:
Healthy IBI: [1000ms, 1000ms, 1000ms, 1000ms]
Unhealthy IBI: [1000ms, 1250ms, 1000ms, 1000ms]
Detected IBI: [1000ms, 1250ms, 1000ms, 1000ms] -> Abnormal
Detected IBI: [1000ms, 950ms, 300ms, 1000ms, 1000ms] -> Abnormal

## Slide 5
      Template-based IBI Prediction
Experiments Results on Real Data:
4,421 pieces of 10-second BSG signal
3,471 pieces of signals with Normal IBI
950 pieces of signals with Abnormal IBI
A ratio of 78.5%
Subject Ratio of
Abnormal Signals

## Slide 6
      Template-based IBI Prediction
Experiments Results on Real Data
950 pieces of signals displaying abnormal IBI are filtered out.
The signals with confirmed normal IBI were used as the baseline to construct a simulated dataset.
Below 4 situations are carefully tested.
Extreme Heart Rate: Instances where heart rate is exceptionally high(HR > HR_max * 0.98).
Abnormalities occurring within a single heartbeat.
Respiratory Sinus Arrhythmia
Signals are of moderate quality. (Only 4 good circles within a 10-second piece)
Extreme Heart Rate

## Slide 7
      Template-based IBI Prediction
Abnormalities occurring within a single heartbeat.
One Abnormal Heartbeat | Mean | Experiment_1 | Experiment_2 | Experiment_3
Add 3.5Hz Sine Wave | 0.967 | 0.946 | 0.964 | 0.991
Add 6Hz Sine Wave | 0.927 | 0.926 | 0.915 | 0.941
Abnormal Data Construction: Add or subtract a random number within the range of 240ms to 480ms from the original IBI.
Abnormal Type | Noise | Mean | Experiment_1 | Experiment_2 | Experiment_3
One Abnormal Heartbeat | Add 3.5Hz Sine Wave | 0.967 | 0.946 | 0.964 | 0.991
 | Add 6Hz Sine Wave | 0.927 | 0.926 | 0.915 | 0.941
Respiratory Sinus Arrhythmia | Add 3.5Hz Sine Wave | 0.983 | 0.987 | 0.979 | 0.983
 | Add 6Hz Sine Wave | 0.960 | 0.958 | 0.970 | 0.925
Respiratory Sinus Arrhythmia

## Slide 8
      Template-based IBI Prediction
Signals are of moderate quality

## Slide 9
      Template-based IBI Prediction
Uniform Distribution of Heartbeats
Diagnosis of Heart Rate Abnormalities:
1. When IBI is entirely accurate and successfully identifies abnormalities.
2. When IBI is not entirely accurate but still successfully identifies abnormalities.
Currently, it's difficult to determine exactly how many IBIs can be accurately identified.
Additionally, it's easier to misinterpret heartbeats that are widely spaced. However, anomalies where the interval between heartbeats shortens are relatively easier to identify.

## Slide 10
Part_2

## Slide 11
      Classification Model
Visualize and analyze the test results of the classification model, attempting to summarize what the model has learned.
Some existing issues:
When slicing, usually only few peaks can be seen, typically around 3-4.
The red line in the graph represents the Mean Template. The reason for this difference is due to the asymmetry in sample quantities. Samples with more data points tend to be smoother.
Based on above 2 reasons, analyzing test results of the classification model suggests that our feature extraction may not be helped.

## Slide 12
Then, I visualized the complete signal slices and attempted to directly extract features related to peaks (mainly amplitudes) in the BSG signal.
The motivation behind this approach stemmed from the core challenge of waveform uncertainty. Additionally, upon observing the image on the right, I speculated whether the waveform evolved based on BP as the independent variable.
However, after reviewing some papers, I realized that this approach might not be feasible.
Signal Type | Core Feature | Feature Type
SCG-PPG | PTT or PAT | Time
ECG-PPG | PTT or PAT | Time
PCG-PPG | PTT or PAT | Time
SCG | AO to AC | Time
BCG | IJK | Amplitude
      Complete Circle Segmentation

## Slide 17
All types of Pulse Transit Times (PTTs) and Pulse Arrival Times (PATs) can be calculated using BCG-PPG signals and SCG-PPG signals. And PAT and PTT are proven to be directly proportional to S and D.
Locating the positions of the J peak/OA peak in the BSG signal or in the derivative of the BSG signal may help us gain a better understanding of the BSG signal.
      Next Step
Problems
About the accuracy of VTCN-based classification model.
2. Peak number of signals.

## Slide 18
Thanks!