## Slide 1
Presentation
Jiayu Chen
2024.07.22

## Slide 2
Outline
Part_1: Our New Model Works Well In Real AFib Data
Part_2: Effects of Improved Method

## Slide 3
Our New Model Works Well In Real Data (3AE4)
Dataset | IoT2023 | Jiayu | Comparison
3AE4_1 | Number:13981 Ratio:81% MAE:6.57 | Number:9765 Ratio: 58% MAE: 3.27 | Ratio -28.3% MAE -50.2%
3AE4_2 | Number: 10971 Ratio: 64% MAE:13.82 | Number:6899 Ratio: 41% MAE:3.58 | Ratio -35.9% MAE -74.1%
3AE4_3 | Number:11285 Ratio:66% MAE:21.75 | Number: 5312 Ratio: 31% MAE: 4.54 | Ratio -53% MAE -79.1%
3AE4_All | Number: 36237 Ratio:70% MAE: 13.58 | Number: 21976 Ratio:43% MAE: 3.69 | Ratio -38% MAE -72.8%
HR Estimation on Real AFib Data
I got 3 datasets of the Afib patient from Zixuan.
Yingjian’s method doesn’t work on this patient, which utilized 70% of all data and achieved 13.58 on MAE. (Figures are on the next page.)
I made some improvements to the original model, which works well, utilizing 43% of all data and achieving 3.69 on MAE.
Attention: I treat this Afib patient as a healthy person and didn’t use the model specially designed for Afib patients(very computationally expensive). The MAE should be smaller than 3 finally.
*Number in the table means useful 10s signal piece after Quality Control. Ratio=Number/All.
Notes: Prof Song, you send me an

## Slide 4
3AE4_1
3AE4_2
3AE4_3
Blue points and yellow points are ground truth and predicted values by Yingjian’s model respectively.
The code Yingjian sent to me should be a little different from the algo implemented in Beddot. Anyway, it doesn’t work well.

## Slide 5
3AE4_1, MAE of IoT: 6.57, MAE of New: 3.27
3AE4_2, MAE of IoT: 13.82, MAE of New: 3.58
3AE4_3, MAE of IoT: 21.75, MAE of New: 4.54

## Slide 6
I made some improvements to the segmentation. After applying this method, the long template containing more than one period, like the above bule lines, won’t appear again. The blue lines above will be replaced by the yellow lines.
Compared to research, this method is more about engineering implementation, but it works so well. HR estimation(MAE) of the Afib patient(3AE4) improved from 5.7 to 3.69.
Effects of Improved Method