## Slide 1
Presentation
Jiayu Chen
2023.12.12

## Slide 2
Work Description
Part_1: A Brief Explanation of the FMM Algorithm
Part_2: Detailed Introduction to the BSG Signal Processing Workflow:
      1. Signal Preprocessing
      2. Periodic Segmentation and Realignment
      3. Template Calculation and Quality Filtering
      4. Attempt at Feature Extraction
      5. Evaluating the Effectiveness of Feature Extraction for Prediction
Part_3: Attempts based on the given suggestions, including Matched Filter, SG Filter, and differentiation
Part_4: Problems

## Slide 3
Part_1

## Slide 4
Part_2

## Slide 5
Signal Preprocessing
呼吸到底要不要
从模拟数据中反映出的结果来看
计算Template的算法，至关重要
好的计算Template算法，可以抵消呼吸带来的影响
Codes implemented by myself from the paper IoT2023
Codes from Yingjian
BCG_Preprocessing.py
过滤掉质量差的信号。
从能够用来预测呼吸和心跳的信号，比能用来提取模板的信号，要更加的杂乱一些。
我和Song老师在上次会议时认为，需要确立合适的标准，再增加一轮的筛选，从而确保信号的质量。
这个筛选的标准，已经解决了，我后面会详细的说
评估策略比我复现出来的代码要松不少
4672信号还剩下4524条信号。
太过严格了
4672条信号筛选结束满足条件的大致472条信号
Problem_1
Problem_2
Conclusion
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
Notes: 之前的通过复现论文“”实现了信号质量检测，并过滤掉质量差的信号。
论文中的过滤方法似乎有一些太过严格了 4672条信号筛选结束满足条件的大致472条信号。
然后拿到了Yingjian学长的源代码，里面的那个质量评估函数。它的评估策略比我复现出来的代码要松不少，4672信号还剩下4524条信号。
我采用了Yingjian的预处理方式。
从能够用来预测呼吸和心跳的信号，比能用来提取模板的信号，要更加的杂乱一些。
我和Song老师在上次会议时认为，需要确立合适的标准，再增加一轮的筛选，从而确保信号的质量。
这个筛选的标准，已经解决了，我后面会详细的说

## Slide 6
面临着两个挑战
- Waveforms sometimes resemble SCG, sometimes resemble BCG, and at times fall between the two.
- 是一个多峰的信号，Amplitudes of peaks within each cycle are not consistent. 不像SCG或者ECG信号，有一个固定的主峰
BCG
SCG
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
Compared to simulated SCG signals, challenges encountered in real signals are as follows:
The initial section of the signal is often problematic, with periodic incompleteness.
      Segmentation
Notes: 挑战1意味着我们设计的分割算法，是能使用在不同类型的信号之上
挑战2意味着，不能像通常那样，定位信号中的一个主峰，然后依据主峰进行分割

## Slide 7
I attempted to utilize an approach presented by Yingjian Song in IoT2023.
While this method is sufficient for estimating heart rate, it is not adequate for accurate segmentation, leading to the following two issues:
Significant and unmanageable errors, making alignment difficult.
The resulting segments are not the desired cycles after the split.
Hilbert transform for envelope
Savitzky-Golay filter
Peak Detection
ACF
Segmentation
Signal
We get
We want
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
      Segmentation

## Slide 8
Solution approach:
Is it possible to transform the multi-peak signal in time domain into a single-peak problem in another domain, and ensure that this single peak is relatively fixed within each cycle?
Upon observation, the distribution of energy density within a single cycle of the signal is often relatively stable.
Transforming the multi-peak signal in the time domain into a single-peak problem in the energy density domain.
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
      Segmentation
Notes: 与希尔伯特变化所取的包络线相比，这种方法有一个非常明确的物理含义，对于某一类周期信号，每个周期中能量集中的位置，是相对稳定的

## Slide 9
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
      Re-alignment
The distribution of energy density is often relatively stable, but not completely identical.
To enhance precision, it is necessary to re-align the signals that have already been segmented.
One-circle pieces
Linear Realignment
Non-Linear Realignment
Linear Alignment -> O(T)
Non-Linear Alignment -> O(T^2)
Acceptable
Unacceptable
There is no need for us.
With phase variation
Without phase variation

## Slide 10
Choose one piece x from N pieces X
Cross Correlation between x and X[1]
Add the Cross Correlation results from N-1 times
Find the appropriate time unit for lag.
Realign piece x.
Re-aligned pieces
Start
Time complexity O(N^3), where N represents the average length of a single cycle.
This algorithm is guaranteed to converge.
Cross Correlation between x and X[N-1]
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
      Re-alignment

## Slide 11
More Figures can be found here:
https://github.com/A-Big-Tortoise/Presentation/tree/main/Pics/Segmentation
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
      Re-alignment

## Slide 12
What kind of signal can extract high-quality template?
Can we check the quality of signals before obtaining the template?
Statistical measurement
Experience-based strategy
If … Else
Yes
No
How to assess whether a template is good or not?
How to eliminate some bad cycles?
Whether the re-alignment is successful can be used to assess the quality of the template.
< Threshold
Low Quality
> Threshold
High Quality
https://github.com/A-Big-Tortoise/Presentation/tree/main/Pics/QualityAssessment4Template
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
      Template and its Quality
对于提取Template这个任务而言，这段信号是不是高质量的呢
Template = Mean( Cycles )
Notes: 这个问题能不能在信号预处理的时候解决？
每个周期之间差异很大
进一步处理，删除掉一些差异很大的周期，进一步过滤信号

## Slide 13
Utilize Tsfresh to extract over 800 features from the template.
Feature cleaning
Drop NaN
Drop features with very small variance.
Drop features with a correlation lower than 0.2.
Linear Regression
CatBoost
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
      Feature Extraction
Linear Regression
CatBoost

## Slide 14
特征提取
IJK
以最大的峰为J峰
I和K峰的相对高度有问题
这种结构，似乎并不在所有的信号中存在
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
      Feature Extraction

## Slide 15
特征提取
IJK
几乎在所有的信号中存在
      Preprocessing
      Segmentation
      Template
Realignment
      Feature Extraction
      Prediction
      Feature Extraction

## Slide 16
Part_3

## Slide 17
An easy experiment about sampling rate.
Model | Data | Sampling Rate | Resample Method | S | D
Template: Mean | Simulation | 100 | - | 1.35 | 4.53
Template: Mean | Simulation | 100->200 | FFT | 0.70 | 2.47
Template: Mean | Simulation | 100->200 | POLY | 0.64 | 2.07
Template: Mean | Simulation | 200 | - | 0.65 | 1.75
The impact of different sampling rates on time series alignment.
Model | Data | Sampling Rate | Resample Method | S | D
Template: Mean | Simulation | 100 | - | 1.35 | 4.53
Template: Mean | Simulation | 100->150 | FFT | 0.95 | 3.24
Template: Mean | Simulation | 100->150 | POLY | 0.95 | 2.98
Template: Mean | Simulation | 150 | - | 0.92 | 2.36
Conclusion:
Resampling signals with low sampling rates can significantly improve the performance. Within a certain range, a higher sampling rate is better.
The resampling mode has a significant impact on the results, with FFT and POLY yielding completely different effects.

## Slide 18
An easy experiment about sampling rate.
Low Sampling Rate
High Sampling Rate
Resample
Principle of accuracy improvement
With the increase in sampling rate, originally relatively separated peaks gradually come closer together.
In addition, the more the number of time points, the higher the fault tolerance.
So the error decreases.

## Slide 19
Part_4

## Slide 20
Cut, realign, and extract templates from real signals.
Signal quality:
For heart rate calculation, the previous filtering algorithm has performed well. However, for template extraction and feature analysis, it is not sufficient and requires an additional filtering layer.
The quality of the signal is in a critical state.
It is possible to extract a template that is barely satisfactory.

## Slide 21
Part_5

## Slide 22
Questions
If we want to precisely understand the BedDot BSG signal, do we need to simultaneously measure a person's SCG, BCG, and BSG signals to explore the relationships between these three signals? Are there any papers that have simultaneously measured SCG and BCG signals? I haven't found relevant papers.
If I were able to propose a segmentation, re-alignment, and innovate an effective template calculation method (with MAE < 3 on SCG simulated signals), and suggest a metric for evaluation, in what field would this likely be presented at a conference?

## Slide 23
Thanks!

## Slide 24
Why doesn’t FMM work
Advantages of FMM (from emails by authors):
“particularly when dealing with pronounced spike waves”
“The FMM model is specifically effective at identifying high peaks against the background noise”
“to detect other less prominent peaks more components could be added.”
Disadvantages of FMM (from the demo code):
We must decompose a single-cycle signal into a large number of components, if we want to focus on smaller peaks.
After decomposition, the relationship between these components becomes chaotic. There is a loss of interpretability in decomposed components.
We can only use FMM to denoise one-circle signal.

## Slide 25
Why doesn’t FMM work
We need to decompose a single-cycle signal into a large number of components, if we want to focus on smaller peaks.
There is almost no interpretability in decomposed components.