## Slide 1
Presentation
Jiayu Chen
2024.02.26

## Slide 2
Work Description
Part_1: Template-based IBI Prediction
Part_2: BP-related Features of PPG
Part_3: Questions

## Slide 3
      Template-based IBI Prediction
Conclusion:
The template-based approach is an effective tool for analyzing arrhythmia, advancing beyond models based on the assumption of a uniform heartbeat distribution.
Currently, a series of experiments have demonstrated its effectiveness. I believe that once the remaining issue is resolved, we can start writing the paper.

## Slide 4
      Template-based IBI Prediction
HR Estimation, MAE | Yingjian | New Method | Rate
All_Back | 1.115 | 1.021 | -9.4%
CTRU_all_data_all_labels, Posture=0 | 1.984 | 2.000 | +0.8%
Conclusion:
The template-based approach is an effective tool for analyzing arrhythmia, advancing beyond models based on the assumption of a uniform heartbeat distribution.
Currently, a series of experiments have demonstrated its effectiveness. I believe that once the remaining issue is resolved, we can start writing the paper.
The dataset all_back is a well-filtered subset.
However, CTRU_all_data_all_labels, on the other hand, was filtered using Yingjian's quality control method instead of more targeted methods, so the performance of the New Method could be further improved in the future.
Experiment 1: HR Estimation

## Slide 5
      Template-based IBI Prediction
Confusion Matrix | Normal | Abnormal
Normal | 548 | 95
Abnormal | 3 | 2519
A 10-second BSG signal can construct a dataset of heart rate anomalies while ensuring a constant heart rate.
The ratio of normal heart rate signals to abnormal heart rate signals in the simulated dataset is approximately 1:4.
Experiment 2: Arrhythmia Classification

## Slide 6
      Template-based IBI Prediction
HR Estimation, MAE | Yingjian | New Method
All Back(all) | 1.115 | 1.021
All Back(healthy) | 1.034 | 
All Back(arrhythmia) | 1.851 | 
Experiment 3
Using the classification algorithm from Experiment 2, the all_back dataset was divided into two parts: one containing normal heart rate signals and the other containing signals classified as abnormal heart rates. It can be concluded that the model is ineffective in handling arrhythmia data, which is the main reason for its inferior performance compared to the template-based method.
HR Estimation, MAE | Yingjian | New Method
All Back (Constructed) | 1.977 | 1.615

## Slide 7
      Template-based IBI Prediction
Experiment 4: IBI Prediction
The IBI calculated from PPG and BSG signals does not strictly correspond, so currently, visualization is used to display the results. The results mainly consist of 4 categories.
Category 1: The trends are consistent.

## Slide 8
      Template-based IBI Prediction
Category 2: The trend doesn't match, but estimated heart rate error is quite small.

## Slide 9
      Template-based IBI Prediction
Category 3: It seems that the error in PPG is larger.

## Slide 10
      Template-based IBI Prediction
Category 4: Quality control of BSG signals needs to be improved.
Conclusion of Experiment 4:
PPG is sometimes not entirely reliable, and there is a phase shift between PPG and BSG. Using IBI obtained from PPG as labels seems inappropriate.
There is a significant difference between HR prediction and IBI prediction in the 10-second signal, indicating the need for stricter quality control to ensure accuracy of each heartbeat interval.

## Slide 11
      Template-based IBI Prediction
Denoised Noisy
Denoised Noisy
MAE of HR
MAE of HR
Experiment 5
Quality control is necessary, but denoising is not essential. Most noise is unrelated, and some noise can actually help us match more accurately.

## Slide 12
      Template-based IBI Prediction

## Slide 13
      BP-related Features of PPG
Model | S (Real/Paper) | D (Real/Paper)
LR | 15.737/12.224 | 8.495/9.204
SVR | 14.905/11.6415 | 7.869/7.617
Template-based Feature Extraction

## Slide 14
      BP-related Features of PPG

## Slide 15
Thanks!