## Slide 1
Weekly Presentation
Jiayu Chen
2023.8.14
Notes: Ok, I will begin my weekly Presentation.

## Slide 2
Work_1: Improve code: DataDemo/simscg.py
>python simscg.py 1 0 90 180 filename
>python simscg.py 1 0.1 90 180 filename
Hr:77 rr:16 sp:101 dp:72
Hr:110 rr:11 sp:167 dp:70
>python simscg.py 1 0 90 180 seed filename
>python simscg.py 1 0.1 90 180 seed filename
Hr:110 rr:11 sp:167 dp:70
Hr:110 rr:11 sp:167 dp:70
New simscg.py is uploaded to https://github.com/A-Big-Tortoise/NRSR_Research/tree/main/Code/new_simscg.py
I hope that helps.
Simulation before codes are improved:
Simulation after codes are improved:
Changing only the noise level produces completely different signals.
Producing the same signal is simply a matter of the absence or presence of the noise.
Notes: My first work is to make some improvements for the simulation of the scg signal.
Prof song you once give us a file called DataDemo, we can use it to simulate scg signals.
It is a little inconvenient for me to use. So I make some improvements.
Before the codes are improved.
Changing only the noise level produces completely different signals. If I want to test the de-noising effect of the algorithm, I have to write codes to add the noise manually.
After the codes are improved.
Producing the same signal is simply a matter of the absence or presence of noise.
It is more convenient to check the de-noising effect of the algorithm.
The new code is uploaded to my github, I hope that helps.

## Slide 3
Work_2: Get Envelope, HR Rate, Segmentation, Clustering
Envelope
Peaks Detection
HR Estimation
Segmentation
Stack
Clean Data
(No Noise, No RR)
Template
K-Shapes Clustering
Heartbeat Rate
Hilbert Transform
Notes: My second work is to try use Hilbert transform to get envelope, use Heartbeat rate to segment signals and finally use K-shapes clustering to get the Template signal.

## Slide 4
Work_2: Get Envelope, HR Rate, Segmentation, Clustering
After removing the noise, the envelope obtained by this method will be perfect.
Segmentation based on HR will cause each segment has different phases.
K-shapes Clustering is particularly suitable for handling this situation.
Create Envelope and Peaks Detection
Segmentation and Clustering
Notes: It is not hard, I just show the result.
The fist picture is about creating envelope and peaks detection.
We can see.
After removing the noise, the envelope obtained by this method will be perfect.
The 2nd picture is about Segmentation and clustering
Segmentation based on HR will cause each segment has different phases.
K-shapes Clustering is particularly suitable for handling this situation.
If noise Are Removed, this pipeline works well.

## Slide 5
Work_3: Implement One Paper: Band Filter, EEMD, PCA and Spectrum Analysis
Band-pass Filter
EEMD / EMD
PCA
Spectrum Analysis
Noisy Data
HR Estimation
PCA
Spectrum Analysis
RR Estimation
IMFs Selection
Notes: Ok, the next is my third work.
I implement one paper. The idea of the paper is pretty simple.
First, the data will be passed through a Band-Pass filter,
and then the data will be decomposed using EEMD or EMD.
Then the decomposed IMFs will be selected by their frequencies.
After selection, PCA and spectral analysis will be performed to obtain the HR and RR Estimation.

## Slide 6
Work_3: Implement One Paper: Band Filter, EEMD, PCA and Spectrum Analysis
Band-pass filter: 0.1 Hz – 8 Hz
EMD and EEMD:
EMD
EEMD
From the perspective of IMF_1 and IMF_2, decomposition effect of EEMD is better.
Choose EEMD!
Notes: Okay, let's go through it quickly.
The pass range of this band-pass filter is ranging from 0.1 Hz to 8 Hz.
The picture is decomposition effects of EMD and EEMD on the same signal.
From the perspective of IMF_1 and IMF_2, decomposition effect of EEMD is better.
Choose EEMD!

## Slide 7
Work_3: Implement One Paper: Band Filter, EEMD, PCA and Spectrum Analysis
Selection of IMFs:
Fusion of IMFs:
Strategy 1: Using only PCA.
Strategy 2: When only one IMF is selected, PCA is not used. The selected IMF is used directly.
Strategy 3: Not using PCA, directly summing up the IMFs.
0.1 Hz < IMFs < 0.75 Hz
0.75 Hz < IMFs < 2.25 Hz
Group2: RR Estimation
Group1: HR Estimation
Num of IMFs in Group1 ranges from 1 to 4
Num of IMFs in Group2 ranges from 1 to 2
The limited number of IMFs in each group makes it difficult for PCA to leverage its advantages, and it might even lead to significant errors!!!
Notes: Next step is the selection of IMFs
IMFs with frequencies between 0.75 Hz and 2.25 Hz are assigned to the first group for HR Estimation.
Number of IMFs in Group1 ranges from 1 to 4
IMFs with frequencies between 0.1 Hz and 0.75 Hz are assigned to the second group for RR Estimation.
Number of IMFs in Group2 ranges from 1 to 2
The limited number of IMFs in each group makes it difficult for PCA to leverage its advantages, and it might even lead to significant errors!!!
AS to the fusion of IMFs, I tried three different strategies.
Strategy 1 is Using only PCA.
Strategy 2 is When only one IMF is selected, PCA is not used. The selected IMF is used directly.
Strategy 3 is Not using PCA, directly summing up the IMFs.

## Slide 8
Work_3: Implement One Paper: Band Filter, EEMD, PCA and Spectrum Analysis
HR ranging from
[50, 150]
RR ranging from
[10, 30]
Conclusions:
In HR estimation, directly summing up IMFs is better, as strategies involving PCA tend to have more outliers.
In RR estimation, 3 strategies have awful performance. This is due to the lack of careful signal denoising (Paper only use band-pass filter).
Notes: Here is the result of using this algo to Noisy signals.
The black box in the graph means the ranges for HR and RR, respectively.
We can get 2 conclusions.

## Slide 9
Work_3: Implement One Paper: Band Filter, EEMD, PCA and Spectrum Analysis
HR ranging from
[50, 150]
RR ranging from
[10, 30]
Conclusions:
After denoising, the performance of HR and RR estimation has significantly improved.
In HR estimation, summing up IMFs shows best results.
In RR estimation, (PCA+SUM) shows best results.
Clean Signal HR Estimation
Clean Signal RR Estimation
Two possible reasons of the inability to achieve the same performance as mentioned in the paper:
1. The original paper used ECG signals rather than SCG signals.
2. The selection of IMFs may differ from the implementation in the original paper.
Notes: Here is the result of using this algo to clean signals.
From these 2 graphs, we can get 3 conclusion:
2. 3.
If use clean signal, this algo seems to work adequately.
Here are Two possible reasons of the inability to achieve the same performance as mentioned in the paper:
1. The original paper used ECG signals rather than SCG signals.
2. The selection of IMFs may differ from the implementation in the original paper.

## Slide 10
Work_4: Clustering Exploration
2 ideas:
Clustering fragments of the raw signal directly, will certain metrics, like S or D, also be clustered accordingly?
Can clustering fragments of the raw signal directly help us improve the accuracy of HR and RR estimation?
I attempted direct clustering of the raw signal and derived five interesting conclusions.
Notes: The next is my forth work, The fourth work originated from two ideas

## Slide 11
Work_4: Clustering Exploration
Conclusion 1: There is a noticeable classification effect on HR, a slight classification effect on S, and no relevance to the other two metrics.
K-Shapes, Num_clusters=2
K-Shapes, Num_clusters=3
Notes: RR and D have no response to clustering.

## Slide 12
Work_4: Clustering Exploration
Conclusion 2: Number of clusters greater than 3 yield no meaningful results.
K-Shapes, Noisy signals
K-Means, Noisy signals
Notes: When number of clusters exceeds 3, various peculiar outcomes arise.

## Slide 13
Work_4: Clustering Exploration
Conclusion 3: K-Shapes >> K-Means
K-Shapes, Noisy signals
K-Shapes, Noisy signals
K-Means, Noisy signals
K-Means, Noisy signals
Notes: K-shapes clustering is much better than K-Means clustering.
We can see from the right 2 graphs that the K-Means clustering results are meaningless and explain nothing

## Slide 14
Work_4: Clustering Exploration
Conclusion 4: The clustering effect is not very sensitive to the length of the intercepted signal, but it should not be too long or too short.
K-Shapes, 300ms
K-Shapes, 600ms
K-Shapes, 1200ms
K-Shapes, 2400ms
0.3
0.6
1.2
2.4
Second
Effect
Clustering effect of signal fragment length with HR metrics (subjective)
The gap is
very small.
Notes: Conclusion 4: The clustering effect is not very sensitive to the length of the intercepted signal, but it should not be too long or too short.
The following four figures show the effect of clustering using K-shapes for signals of lengths of 300ms, 600ms and so on
You can see that the clustering performs best with a 600ms length signal. But the difference with the others is not big
Below is a line graph about Clustering effect of signal fragment length with HR metrics (subjective)
I think the gap between performance is very small.

## Slide 15
Work_4: Clustering Exploration
Conclusion 5: The clustering effects are not sensitive to noise.
K-Shapes，1200ms
Noisy
Noisy
No Noise
No Noise
I checked codes, the clustering results are the same, whether or not there is 0.1dB noise.
Notes: Conclusion 5: Not sensitive to noise
The following figure shows the results of k-shapes clustering on a 1200ms signal, with noisy signals on the left and clean signals on the right
I checked codes, the clustering results are the same, whether or not there is 0.1dB noise.

## Slide 16
Work_4: Clustering Exploration
Subsequently, I tried clustering on the templates I got earlier as well.
Conclusion1： The clustering effect on HR and S, the improvement is slight.
Still so no effect for RR and D.
Conclusion2：K-Shapes >> K-Means
K-Shapes, Templates
K-Means, Templates
Notes: Subsequently, I tried clustering on the templates I got earlier as well.
Conclusion1： The clustering effect on HR and S, the improvement is slight.
Still so no effect for RR and D.
Conclusion2：K-Shapes >> K-Means

## Slide 17
Work_5: Tutorial
Features:
Statistical
Temporal
Spectral
Now:
Input: 1-D signal (N, )
Next Step:
Input: 2-D signal (M, N)
Progress:
(8/8)
(11/15)
(15/20)
Filter (Butter, Chebyshev, Bessel)
EMD & EEMD
Denoising(FFT & Wavelet)
Clustering(K-Means, K-Shapes, Hierarchical clustering )
Extraction of Common Features in Signal Processing
Notes: Tutorial is divided into two parts,
the first part is the extraction of common features in signal processing.
It includes statistical features, Temporal features, and Spectral features.
Right now these functions only support one-dimensional data inputs,
the next step is to try to use matrix calculations to make them run two-dimensional inputs
The second part, which is a tutorial of commonly used algorithms,
like three common filters, EEMD EMD

## Slide 18
Work_6: Theoretical knowledge Learning
Signals and Systems
Course: EE120, Berkeley
This week's progress:
Lecture 8 (discrete-time Fourier transform)
Lecture 9 (discrete-time Fourier transform, continued)
Finish 1 lab
Next week’s plan:
Lecture 10 (the DFT; FIR filters)
Lecture 11 (Fourier transforms in two dimensions)
Finish 1 lab
Application Materials
This week's progress:
Statement of Purpose: 100 %
Writing Sample: 90 %
Today: Submit

## Slide 19
Questions
How can I alone judge whether a method works or not, when I don't clearly understand its principles. For example, use the Hilbert transform to extract the envelope. I failed last time and then after your guidance succeeded this time.
The S is weakly responsive to clustering. Is it possible use clustering to divide S into several large ranges? Does that make sense?

## Slide 20
Questions About Application

## Slide 21
Thanks!